## Slide 1: Verilog & FPGA
Digital Design

## Slide 2: Standard HDL languages
Standards HDL (hardware description language) languages
  Verilog
    1984: Gateway Design Automation Inc.
    1990: Cadence -> Open Verilog International
    1995: IEEE standardization
    2001: Verilog 2001
  VHDL
    1983-85: IBM, Texas Instruments
    1987: IEEE standardization
    1994: VHDL-1993

## Slide 3: Other HDL languages
HDL development is very time consuming compared to software development
Lot of programmers with C/C++ knowledge, much less HDL designer
High level hardware description languages
  Celoxica Handel-C: based on ANSI-C with special features
  SystemC: standardized, object oriented C++ based language
  Mentor Catapult-C: can generate hardware from standard C code
Faster simulation, verification
HW/SW co-design

## Slide 4: Purpose of HDL languages
Modeling hardware behavior
  Large part of these languages can only be used for simulation, not for hardware generation (synthesis)
  Synthesizable part depends on the actual synthesizer
Replace graphical, schematic based design method (which very time consuming)
RTL (Register Transfer Level) level description
  Automatic hardware synthesis
  Increase productivity

## Slide 5: HDL languages
Modular languages
HDL module
  Input and output port definitions
  Logic equations between the inputs and the outputs
Unlike software programming languages, NOT a sequential language
  Describes PARALLEL OPERATIONS

## Slide 6: Modules
Building blocks to design complex, hierarchical systems
Hierarchical description, partitioning

## Slide 7: Verilog Syntax
Comments (like C)
  // one line
  /* */ multiple lines
Constants
  <bit width><‘base><value>
    5’b00100: 00100 decimal value: 4, 5 bit wide
    8’h4e: 01001110 decimal value: 78, 8 bit wide
    4’bZ: ZZZZ high impedance state

## Slide 8: Verilog: module (2001)
„module” keyword
„module” name
Input ports
Output ports
„endmodule”
keyword
Functional
description
module test(
input clk,
input [7:0] data_in,
output [7:0] data_out,
output reg valid
);
…….
…….
…….
endmodule

## Slide 9: Verilog: module
module test(clk, data_in, data_out, valid);
input clk;
input [7:0] data_in;
output [7:0] data_out;
output reg valid;
…….
…….
…….
endmodule
„module” keyword
„module” name
Port list
(without type)
„endmodule”
keyword
Port types

## Slide 10: Bit operations
~, &, |, ^, ~^ (negate, and, or, xor, xnor)
Bitwise operator on vectors, e.g.:
  4’b1101 & 4’b0110 = 4’b0100
If the operand widths are not equal, the smaller one is extended with zeros
  2’b11 & 4’b1101 = 4’b0001
(Logic operators: !, &&, ||)

## Slide 11: Bit reduction operators
Operates on all bits of a vector, the output is a single bit
&, ~&, |, ~|, ^, ~^ (and, nand, or, nor, xor, xnor)
  &4’b1101 = 1’b0
  |4’b1101 = 1’b1
  Typical usage scenarios:
    Parity check

## Slide 12: Comparison
Same as in C
Equal, not-equal
  ==, !=
  ===: equality considering „Z”, „X”
  !==: not-equal considering „Z”, „X”
Comparison
  <, >, <=, >=

## Slide 13: Arithmetic
Same as in C
Operators: +, -, *, /, %
  Not all of them is synthesizable
    E.g. division, modulo are only synthesizable when the second operator is power of 2
  Negative numbers in twos-complement code

## Slide 14: Other operators
Concatenate: {} E.g.:
  {4’b0101, 4’b1110} = 8’b01011110
Shift:
  <<, >>
Bit selection
  Selected part has to be constant
  data[5:3]

## Slide 15: Data types
wire
  Behaves like a real wire (combinatorial logic)
  Declaration of an 8 bit wire: wire [7:0] data;
reg
  After synthesis it can translate into
    Wire
    Latch
    Flip-flop
  E.g.: reg [7:0] data;

## Slide 16: Assign
Assign can be used only on wire types
Continuous assignment
  Left operand continuously gets a new value
E.g.
  assign c = a & b;
Only one assign can drive a single variable
Multiple assigns operate parallel to each other
Can be used to describe combinatorial logic

## Slide 17: Always block
Syntax:
A variable should be written only in one always block
The sensitivity list cannot contain the outputs (left-side variables) of the always block
Assign cannot be used within an always block
Multiple always blocks are executed in parallel
always @ (….)
begin
…..
…..
end
Sensitivity list
Operations

## Slide 18: Always – assignments
Blocking: =
  Blocks the execution of operations after it till it is executed -> sequential operation (don’t use it unless really necessary)
Nonblocking: <=
  Nonblocking assignments are executed in parallel -> hardware-like operation
Always use nonblocking assignment

## Slide 19: Always – Flip Flop
Flip Flop: edge sensitive storage element
Synchronous reset
Asynchronous reset
always @ (posedge clk)
if (rst)
c <= 1'b0;
else
c <= a & b;
always @ (posedge clk)
c <= a & b;
always @ (posedge clk, posedge rst)
if (rst)
c <= 1'b0;
else
c <= a & b;

## Slide 20: Always – Flip Flop
In Xilinx FPGAs
  Reset and set can be synchronous or asynchronous
  Priority in synchronous case:
    reset, set, ce
Asynchronous example:
always @ (posedge clk, posedge rst, posedge set)
if (rst)
c <= 1'b0;
else if (set)
c <= 1'b1;
else if (ce)
c <= a & b;

## Slide 21: Always – comb. logic
Result is continuously calculated – if any of the inputs changes the output immediately changes
always @ (a, b)
c <= a & b;
always @ (*)
c <= a & b;

## Slide 22: Always – latch
Latch: level sensitive storage element
  as long as the „gate” input is ‘1’, the input is sampled into the latch
  If the „gate” input is ‘0’, the previously sampled value is kept
always @ (*)
If (g)
c <= a & b;

## Slide 23: Always – latch error
Using latch is typically a bad idea; it can be generated by wrong code
  Not full if or case statements
  Synthesizers typically give a warning
always @ (*)
case (sel)
2’b00: r <= in0;
2’b01: r <= in1;
2’b10: r <= in2;
endcase
always @ (*)
if (sel==0)
r <= in0;
else if (sel==1)
r <= in1;
else if (sel==2)
r <= in2;

## Slide 24: Always – correct if/case
Correct code using combinatorial if/case
always @ (*)
case (sel)
2’b00: r <= in0;
2’b01: r <= in1;
2’b10: r <= in2;
default: r <= ‘bx;
endcase
always @ (*)
if (sel==0)
r <= in0;
else if (sel==1)
r <= in1;
else
r <= in2;

## Slide 25: Blocking – nonblocking (1)
reg t, r;
always @ (posedge clk)
begin
t <= a & b;
r <= t | c;
end
reg t, r;
always @ (posedge clk)
begin
t = a & b;
r = t | c;
end
reg t, r;
always @ (posedge clk)
begin
r = t | c;
t = a & b;
end

## Slide 26: Blocking – nonblocking (2)
reg t, r;
always @ (posedge clk)
begin
t = a & b;
r <= t | c;
end
reg t, r;
always @ (posedge clk)
begin
t <= a & b;
r = t | c;
end

## Slide 27: Blocking – nonblocking (3)
reg s2, s3;
always @ (posedge clk)
begin
s2 <= in0 + in1;
s3 <= s2 + in2;
end
reg s0, s1;
always @ (posedge clk)
begin
s0 = in0 + in1;
s1 = s0 + in2;
end
Eg. 3 input adder
reg s4;
always @ (posedge clk)
begin
s4 <= in0 + in1 + in2;
end

## Slide 28: Structural description
Creating hierarchy: connecting modules
Port – signal assignment based on the port names
module top_level (input in0, in1, in2, output r);
wire xor0;
xor_m xor_inst0(.i0(in0), .i1(in1), .o(xor0));
xor_m xor_inst1(.i0(xor0), .i1(in2), .o(r));
endmodule

## Slide 29: Example – MUX (1.)
2:1 multiplexer
module mux_21 (input in0, in1, sel, output r);
assign r = (sel==1’b1) ? in1 : in0;
endmodule
module mux_21 (input in0, in1, sel, output reg r);
always @ (*)
if (sel==1’b1) r <= in1;
else r <= in0;
endmodule
module mux_21 (input in0, in1, sel, output reg r);
always @ (*)
case(sel)
1’b0: r <= in0;
1’b1: r <= in1;
endmodule

## Slide 30: Example – MUX (2.)
4:1 multiplexer
module mux_41 (input in0, in1, in2, in3, input [1:0] sel, output reg r);
always @ (*)
case(sel)
2’b00: r <= in0;
2’b01: r <= in1;
2’b10: r <= in2;
2’b11: r <= in3;
endcase
endmodule

## Slide 31: Example – 1 bit full adder
module add1_full (input a, b, cin, output cout, s);
xor3_m xor(.i0(a), .i1(b), .i2(cin), .o(s));
wire a0, a1, a2;
and2_m and0(.i0(a), .i1(b), .o(a0));
and2_m and1(.i0(a), .i1(cin), .o(a1));
and2_m and2(.i0(b), .i1(cin), .o(a2));
or3_m or(.i0(a0), .i1(a1), .i2(a2) , .o(cout))
endmodule
module add1_full (input a, b, cin, output cout, s);
assign s = a ^ b ^ cin;
assign cout = (a & b) | (a & cin) | (b & cin);
endmodule
module add1_full (input a, b, cin, output cout, s);
assign {cout, s} = a + b + cin;
endmodule

## Slide 32: Example – 4 bit adder, structural
module add4 (input [3:0] a, b, output [4:0] s);
wire [3:0] cout;
add1_full add0(.a(a[0]), .b(b[0]), .cin(1'b0), .cout(cout[0]), .s(s[0]));
add1_full add1(.a(a[1]), .b(b[1]), .cin(cout[0]), .cout(cout[1]), .s(s[1]));
add1_full add2(.a(a[2]), .b(b[2]), .cin(cout[1]), .cout(cout[2]), .s(s[2]));
add1_full add3(.a(a[3]), .b(b[3]), .cin(cout[2]), .cout(s[4]), .s(s[3]));
endmodule
module add4 (input [3:0] a, b, input cin, output cout, output [3:0] sum);
assign {cout, sum} = a + b + cin;
endmodule

## Slide 33: Example – 4 bit adder, structural

## Slide 34: Example – 4 bit adder, RTL

## Slide 35: Example – Shift register
16 bit deep shift register (e.g. for delaying a value)
module shr (input clk, sh, din, output dout);
reg [15:0] shr;
always @ (posedge clk)
if (sh)
shr <= {shr[14:0], din};
assign dout = shr[15];
endmodule

## Slide 36: Example – Counter
Binary counter with synchronous reset, clock enable, load and direction inputs
module m_cntr (input clk, rst, ce, load, dir,
input [7:0] din,
output [7:0] dout);
reg [7:0] cntr_reg;
always @ (posedge clk)
if (rst)
cntr_reg <= 0;
else if (ce)
if (load)
cntr_reg <= din;
else if (dir)
cntr_reg <= cntr_reg – 1;
else
cntr_reg <= cntr_reg + 1;
assign dout = cntr_reg;
endmodule

## Slide 37: Example – Secundum counter
50 MHz clock frequency, 1 sec = 50 000 000 clocks
module sec (input clk, rst, output [6:0] dout);
reg [25:0] clk_div;
wire tc;
always @ (posedge clk)
If (rst)
clk_div <= 0;
else
if (tc)
clk_div <= 0;
else
clk_div <= clk_div + 1;
assign tc = (clk_div == 49999999);
reg [6:0] sec_cntr;
always @ (posedge clk)
If (rst)
sec_cntr <= 0;
else if (tc)
if (sec_cntr==59)
sec_cntr <= 0;
else
sec_cntr <= sec_cntr + 1;
assign dout = sec_cntr;
endmodule

## Slide 38: Tri-state lines
Bi-directional buses, eg.
  E.g. data bus of external memories
The bus drive enable signal is critical (bus_drv), take care when generating it
module tri_state (input clk, inout [7:0] data_io);
wire [7:0] data_in, data_out;
wire bus_drv;
assign data_in = data_io;
assign data_io = (bus_drv) ? data_out : 8’bz;
endmodule

## Slide 39: FSM – Finite State Machine
FSM – to create complex control machines
General structure
State register: state variable
Next state function: determines the next state (combinatorial logic)
Output function: generates outputs
  Moore: based on the state register
  Mealy: based on the state registers and the current inputs

## Slide 40: FSM example
Traffic light (simple)
  States: red, yellow, green, red-yellow (no blinking yellow)
  Inputs: timers for the different states
  Output: state

## Slide 41: FSM example – Verilog (1)
module light(
input clk, rst,
output reg [2:0] led);
parameter RED = 2'b00;
parameter RY = 2'b01;
parameter GREEN = 2'b10;
parameter YELLOW = 2'b11;
reg [15:0] timer;
reg [1:0] state_reg;
reg [1:0] next_state;
always @ (posedge clk)
if (rst)
state_reg <= RED;
else
state_reg <= next_state;
always @ (*)
case(state_reg)
RED: begin
if (timer == 0)
next_state <= RY;
else
next_state <= R;
end
RY: begin
if (timer == 0)
next_state <= GREEN;
else
next_state <= RY;
end
YELLOW: begin
if (timer == 0)
next_state <= RED;
else
next_state <= YELLOW;
end
GREEN: begin
if (timer == 0)
next_state <= YELLOW;
else
next_state <= GREEN;
end
default:
next_state <= 3'bxxx;
endcase

## Slide 42: FSM example – Verilog (2)
always @ (posedge clk)
case(state_reg)
RED: begin
if (timer == 0)
timer <= 500; //next_state <= RY;
else
timer <= timer - 1;
end
RY: begin
if (timer == 0)
timer <= 4000; //next_state <= GREEN;
else
timer <= timer - 1;
end
YELLOW: begin
if (timer == 0)
timer <= 4500; //next_state <= RED;
else
timer <= timer - 1;
end
GREEN: begin
if (timer == 0)
timer <= 500; //next_state <= YELLOW;
else
timer <= timer - 1;
end
endcase
Timer
  Loads a new value when state changes
  Down-counter
  ==0: state change
always @ (*)
case (state_reg)
RY : led <= 3'b110;
RED: led <= 3'b100;
YELLOW: led <= 3'b010;
GREEN: led <= 3'b001;
default: led <= 3’b100;
endcase
endmodule

## Slide 43: Parameterized modules
Parameterized adder
Instantiating the parameterized module
module add(a, b, s);
parameter width = 8;
input [width-1:0] a, b;
output [width:0] s;
assign s = a + b;
endmodule
wire [15:0] op0, op1;
wire [16:0] res;
add #(
.width(16)
)
add_16(
.a(op0),
.b(op1),
.s(res)
);

## Slide 44: Simulation
Testbench creation: two possibilities in Xilinx ISE
  Testbench Waveform
    Generating inputs using a GUI
  Verilog Test Fixture
    Generating inputs using Verilog
Simulator
  ISE Simulator
  Modelsim (MXE)

## Slide 45: Verilog Test Fixture
Test Fixture
  Test Fixture is a Verilog module
  The module under test is a sub-module of the test fixture
  All Verilog syntax constructs can be used
  There are non-synthesizable constructs
Time base
  ‘timescale 1ns/1ps
    Time base is 1 ns
    Simulation resolution: 1 ps

## Slide 46: Test Fixture - initial
„initial” block
  Execution starts at time „0”
  Executed once
  „initial” blocks are executed in parallel with each other and with always blocks and assigns
The delays are cumulative, e.g.
initial
begin
a <= 0;
#10 a <= 1;
#25 a <= 2;
#5 a <= 0;
end

## Slide 47: Test Fixture - always
Generating clock
Clocked inputs (propagation time!)
initial
clk <= 1;
always #5
clk <= ~clk;
initial cntr <= 0;
always @ (posedge clk)
#2 cntr <= cntr + 1;

## Slide 48: Task
Declaration:
  In the module which uses the task
  In a different file (more modules can use the same task)
Arbitrary number of inputs and outputs
Can contain timing
Variables declared in a task are local variables
Global variables can be read or written by the task
A task can call another task

## Slide 49: Example - Task
Simulating an asynchronous read operation
Verilog code
task bus_w(input [15:0] addr, input [7:0] data);
begin
xaddr <= addr;
#5 xdata <= data;
#3 xwe <= 0;
#10 xwe <= 1;
while (xack != 1) wait;
#4 xdata <= 8’bz;
xaddr <= 0;
end
endtask;

## Slide 50: Example - Task
„bus_w” is located in „tasks.v” file
x* variables used by the task are global variables defined in the test fixture
Using the task in a test fixture
  3 write cycles
  10 ns between them
`include “tasks.v”
initial
begin
bus_w(16’h0, 8’h4);
#10 bus_w(16’h1, 8’h65);
#10 bus_w(16’h2, 8’h42);
end

## Slide 51: File operations
Reading data into an array
Writing data into a file
reg [9:0] input_data[255:0];
initial
$readmemh(“input.txt”, input_data);
integer file_out;
wire res_valid;
wire [16:0] res;
initial
file_out =$fopen(“output.txt");
always @ (posedge clk)
if (out_valid)
$fwrite(file_out, "%d \n", res);

## Slide 52: FPGAs
FPGA: Field Programmable Gate Array
  Programmable logic devices
Manufacturers: Xilinx, Altera, Actel, Quicklogic, Lattice
Features
  Function is defined by the configuration
  Configuration can be modified, changed
  Complexity
    50000 – 8000000 system gates
    100 – 600 I/O pins
    100 – 400 MHz operating frequency (design dependant)
  Architecture: e.g. RAM or MUX based

## Slide 53: Xilinx FPGAs
Different families
  Spartan: efficient, low cost
  Virtex: more complex, higher performance, extended features
Architecture:
  CLB: configurable logic block
  IOB: I/O block
  BlockRAM: internal memory
  Multiplier, DSP block
  Clock resources: DCM, dedicated clock routing
  Embedded PowerPC processor
  Routing resources

## Slide 54: Xilinx FPGA: configuration
Configuration (CLB content, routing, connections, other parameters) is stored in SRAM
Configuration is lost when there is no power supply
Configuration must be loaded after power-up
  From EEPROM automatically
  Through a development cable (JTAG)

## Slide 55: Xilinx FPGAs – primitives
Using FPGA primitives:
  The internal building blocks of the FPGA can be accessed as a primitive -> can be used as an HDL module
  For most primitives synthesizers can infer them from the appropriate register transfer level HDL description

## Slide 56: Xilinx FPGAs
Implemented design: logic + routing

## Slide 57: Xilinx FPGAs – CLB
Each CLB consists of 4 slices
Slice:
  2 LUTs: look up table, used to implement
    Combinatorial logic functions
    Small ROM and RAM
    Efficient shift registers
  2 Storage elements: configured to FF or latch
    Control signals (set, reset, ce) are shared within a slice
  Dedicated multiplexer (MUXFx)
  Fast carry logic (MUXCY, XORCY)

## Slide 58: Xilinx FPGA: basic logic element
Simple schematic of a slice
4-input LUT: Look-Up Table
  16x1 bit memory
  Address: inputs of the logic equation
  Content: truth table
  Can implement any 4 input logic equation

## Slide 59: Half-slice (4 input LUT)
Spartan series, and Virtex series (excluding Virtex-5)

## Slide 60: Half-slice (6 input LUT)
Virtex-5

## Slide 61: LUT ROM
ROM (asynchronous)
  HDL code
  Xilinx primitives
    ROM16X1, ROM32x1,…..
module rom16 (input [3:0] address, output reg [7:0] data);
always @ (*)
case(address)
4’b0000: data <= CONSTANT0;
4’b0001: data <= CONSTANT1;
……
4’b1111: data <= CONSTANT15;
endcase
endmodule

## Slide 62: LUT RAM
RAM: synchronous write, asynchronous read
  HDL code
  Xilinx primitives
    Single port: RAM16X1S, …..
    Dual port: RAM16X1D, …..
module ram16 (input clk, we, input [3:0] addr, input [7:0] din,
output [7:0] dout);
reg [7:0] mem[15:0];
always @ (posedge clk)
if (we)
mem[addr] <= din;
assign dout = mem[addr];
endmodule

## Slide 63: LUT RAM timing
Read: asynchronous
  Address generated with a counter
Write: synchronous
  Write happens at the marked rising clock edges

## Slide 64: Shift register
LUT based, output addressable shift register
  HDL code
  NO reset input
  Xilinx primitives
    SRLC16, SRLC16E, SRLC32, SRLC32E
module shr_16x1 (input clk, sh, din, input [3:0] addr,
output dout);
reg [15:0] shr;
always @ (posedge clk)
if (sh)
shr <= {shr[14:0], din};
assign dout = shr[addr];
endmodule

## Slide 65: Shift register array
module shr_16x8 (input clk, sh, input [3:0] addr, input [7:0] din,
output [7:0] dout);
reg [7:0] shr[15:0];
integer i;
always @ (posedge clk)
if (sh)
begin
shr[0] <= din;
for (i=15; i>0, i=i-1) begin
shr[i] <= shr[i-1];
end
end
assign dout = shr[addr];
endmodule

## Slide 66: BlockRAM
Synchronous dual-port memory
  Depth: 16384 + 2048 (parity) bit
  Data width: 1, 2, 4, 9, 18, 36 bit
Ports:
  CLK, WE, EN, SSR (clock, write enable, enable, synchronous reset)
  ADDR, DI, DO (address, data in, data out)
  All inputs are synchronous
  Output changes 2-3 ns after the clock edge
Xilinx primitives
  Single port: RAMB16_S1…RAMB16_S36
  Dual port: RAMB16_S1_S1…RAMB16_S36_S36

## Slide 67: BlockRAM timing
Read: synchronous
  Address generated by a counter
Write: synchronous
  Write happens at the marked rising clock edges

## Slide 68: Read-Write collision
Output during an active write operation
  Does not change (NO_ CHANGE)
  Previous data is presented (READ_FIRST)
  New data is presented (WRITE_FIRST)
In dual-port configuration the output of the non-write port is invalid during write cycles (except in READ_FIRST mode)
Writing to the same address from both ports is forbidden

## Slide 69: BlockRAM using primitive
RAMB16_S9 #(
.INIT(9'h000), // Value of output RAM registers at startup
.SRVAL(9'h000), // Output value upon SSR assertion
.WRITE_MODE("WRITE_FIRST")
) RAMB16_S9_inst (
.DO(DO), // 8-bit Data Output
.DOP(DOP), // 1-bit parity Output
.ADDR(ADDR), // 11-bit Address Input
.CLK(CLK), // Clock
.DI(DI), // 8-bit Data Input
.DIP(DIP), // 1-bit parity Input
.EN(EN), // RAM Enable Input
.SSR(SSR), // Synchronous Set/Reset Input
.WE(WE) // Write Enable Input
);

## Slide 70: SP BlockRAM – Read First
module sp_ram(input clk, input we, input en, input [10:0] addr,
input [ 7:0] din, output [7:0] dout);
reg [7:0] memory[2047:0];
reg [7:0] dout_reg;
always @ (posedge clk)
if (en)
begin
if (we)
memory[addr] <= din;
dout_reg <= memory[addr];
end
assign dout = dout_reg;
endmodule

## Slide 71: SP BlockRAM – Write First
module sp_ram(input clk, input we, input en, input [10:0] addr,
input [ 7:0] din, output [7:0] dout);
reg [7:0] memory[2047:0];
reg [7:0] dout_reg;
always @ (posedge clk)
if (en)
begin
if (we)
memory[addr] = din;
dout_reg = memory[addr];
end
assign dout = dout_reg;
endmodule

## Slide 72: SP BlockRAM – No Change
module sp_ram(input clk, input we, input en, input [10:0] addr,
input [ 7:0] din, output [7:0] dout);
reg [7:0] memory[2047:0];
reg [7:0] dout_reg;
always @ (posedge clk)
if (en)
begin
if (we)
memory[addr] <= din;
else
dout_reg <= memory[addr];
end
assign dout = dout_reg;
endmodule

## Slide 73: DP BlockRAM
module dp_ram(input clk_a, we_a, en_a, clk_b, we_b, en_b,
input [10:0] addr_a, addr_b,
input [ 7:0] din_a, din_b, output [7:0] dout_a, dout_b);
reg [7:0] memory[2047:0];
reg [7:0] dout_reg_a, dout_reg_b;
always @ (posedge clk_a)
if (en_a)
begin
if (we_a)
memory[addr_a] <= din_a;
dout_reg_a <= memory[addr_a];
end
assign dout_a = dout_reg_a;
always @ (posedge clk_b)
if (en_b)
begin
if (we_b)
memory[addr_b] <= din_b;
dout_reg_b <= memory[addr_b];
end
assign dout_b = dout_reg_b;
endmodule

## Slide 74: Multiplier: 18x18, signed
HDL
  Combinatorial
  Synchronous
Xilinx primitives
  MUL18X18, MUL18X18S
module mul_c (input signed [17:0] a, b, output signed [35:0] p);
assign p = a*b;
endmodule
module mul_s (input clk, en, input signed [17:0] a, b, output reg signed [35:0] p);
always @ (posedge clk)
if (en)
p <= a*b;
endmodule